## Slide 1: Real Time Model Checking, Performance Evaluation, Synthesis and Optimization
Kim G. Larsen
Aalborg University, DENMARK
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAAAAA
Notes: DG
Verification and Validation of Real-Time and Embedded Systems Professor Kim G Larsen CISS, Aalborg University Denmark Model-driven development has been proposed as a way to deal with the increasing complexity of real-time and embedded systems, while reducing the time and cost to market. The use of models should permit early assessment of the functional correctness of a given design as well as requirements for resources (e.g. energy, memory, and bandwidth) and real-time and performance guarantees. In the lecture we will introduce the tool UPPAAL providing an integrated environment for modeling, validation, verification and synthesis of real-time systems modeled as networks timed automata, extended with data types and user-defined functions. The lectures will provide details on the expressive power of timed automata in relationship to embedded systems as well as details on the power and working of the UPPAAL verification engine. Particular attention will be given to the theory of the underlying formalisms of UPPAAL, including timed automata, priced timed automata, and (priced) timed games addressing a number of associated decision problems related to model-checking and optimal scheduling and strategies. Also, the frontier of decidability will be drawn including pointing out a number of open problems. The lectures will also emphasize the research effort in design algorithms and datastructures for efficient analysis on practical and industrial cases.
FSEN’09
This talk will introduce various recent extensions of the by know well-established formalism of timed automata. The talk apply these extension to verification, optimal scheduling, performance analysis and controller synthesis of real-time and embedded systems. The timed automata extensions considered -- priced timed automata, game timed automata as well as probabilistic timed automata -- are all supported by various branches of the real-time verificaiton tool UPPAAL (www.uppaal.com) which will be demonstrated during the talk. Also, the development of algorithms and datastructures applied by UPPAAL for the efficient analysis of these models is provided.
Validation, Performance Analysis and Synthesis of Embedded Systems Kim G Larsen Within the upcoming European Joint Technology Initiative ARTEMIS as well as several national initiatives such as CISS (www.ciss.dk) and DaNES (http://www.danes.aau.dk/), model-driven development is a key to dealing with the increasing complexity of embedded systems, while reducing the time and cost to market. The use of models should permit early assessment of the functional correctness of a given design as well as requirements for resources (e.g. energy, memory, and bandwidth) and real-time and performance guarantees. Thus, there is a need for quantitative models allowing for timed, stochastic and hybrid phenomenas to be modeled an analysed. UPPAAL and the branches CORA and TIGA provide an integrated tool environment for modelling, validation, verification and synthesis of real-time systems modelled as networks timed automata, extended with data types and user-defined functions. The talk will provide details on the expressive power of timed automata in relationship to embedded systems as well as details on the power and working of the UPPAAL verification engine. In this talk we demonstrate how UPPAAL has been applied to the validation, performance analysis and synthesis of embedded control problems. The applications include so-called task graph scheduling and MPSoC systems consisting of application software running under different RTOS on processors interconnected through an on-chip network. Also we show how CORA and TIGA has been used to synthesize optimal (e.g. wrt. energy or memory) scheduling strategies given applications, including Dynamic Voltage Scaling and a climate controller.

## Slide 2: From Computer Science to Embedded Systems
Notes: IDEA4CPS is rooted in Theoretical Computer Science .. You now the science where skilled programmers and operators can make very big computers do complex calculations of typically high scientific importance .. This I guess I Arne in the old Data Center. We actually still have such big instalments doing HPC – PC clusters or GRIDS.
The underlying foundation here is that of “computable functions” – i.e. a computing system can be understood as a function from input to output and the art is now to prove that you function implemented by a particular program does the right thing. Denotational and Axiomatic Semantics, Abstract Interpretation .. Etc are usefull. BRICS .. Perhabs ..
The first step toward taking computers and programs out of the clean room is that of embedded systems. Here dedicated computers and programs monitor and control a particular proces .. The underlying foundation here is that “reactive system”, the system is understood in term sof its interaction with the environment. Concurrency theory.

## Slide 3: From Computer Science to Cyber Physical Systems
New Foundation
Discrete Models
(Boolean correctness)

Quantitive Models
(time, resources,
probabilistic, stochastic,
continuous,..)
(Quantitative correctness)
Stochasticity
Real Time
Resources
Hybrid
Discrete
Notes: Cyber-Physical Systems is like embedded systems on speed – or several embedded systems interacting in a loose typically adhoc network.
Examples found in future devices in homes … telemedicin. Not just software in the individual car but also interaction between cars for fast mauvering or safe manuvering (collisiton avoidance) – or large intelligent sensor networks in stables.
Properties – need for foundation!
A trend – US invented Cyber Physical Sysstems; China has launced a big initiative and also Germany is planning an initiative
Happy that we can contribute

## Slide 4: Models
ALW( OFF) EVENs<3, p>0.90 ON)
ALW( OFF) EVEN ON)
ALW( OFF) EVENt<5, p>0.90 ON)
ALW( T<3) EVENt<20, p>0.90 T>20)
Discrete
Probabilistic
Timed
Hybrid

## Slide 5: UPPAAL Tool Suit
TRON
CLASSIC
TIGA
CORA
ECDAR
SMC
Optimization
Synthesis
Component
Testing
Performance
Analysis
Verification
STRATEGO
Optimal Synthesis

## Slide 6: Contributors
@UPPsala
  Wang Yi
  Paul Pettersson
  John Håkansson
  Anders Hessel
  Pavel Krcal
  Leonid Mokrushin
  Shi Xiaochun
@AALborg
  Kim G Larsen
  Alexandre David
  Marius Mikucionis
  Gerd Behrman
  Arne Skou
  Brian Nielsen
  Jacob I. Rasmussen
  Thomas Chatain
@Elsewhere
  Emmanuel Fleury, Didier Lime, Johan Bengtsson, Fredrik Larsson, Kåre J Kristoffersen, Tobias Amnell, Thomas Hune, Oliver Möller, Elena Fersman, Carsten Weise, David Griffioen, Ansgar Fehnker, Frits Vandraager, Theo Ruys, Pedro D’Argenio, J-P Katoen, Jan Tretmans, Judi Romijn, Ed Brinksma, Martijn Hendriks, Klaus Havelund, Franck Cassez, Magnus Lindahl, Francois Laroussinie, Patricia Bouyer, Augusto Burgueno, H. Bowmann, D. Latella, M. Massink, G. Faconti, Kristina Lundqvist, Lars Asplund, Justin Pearson...
Notes: Here you see all the contributers over the years.

## Slide 7: Overview
Timed Automata / UPPAAL
  Verification
Stochastic Priced Timed Automata / UPPAAL SMC
  Performance Evaluation
  SMC in a Nutshell
  Stochastic Hybrid Automata
Timed Games / UPPAAL TIGA
  Controller Syntesis
Stochastic Priced Timed Games / UPPAAL STRATEGO
  Optimal & Safe Synteses
Conclusion
  Schedulability Analysis
  Production Cell, .., HYDAC Case
  Adaptive Cruice Control

## Slide 8: Timed Automata

## Slide 9: A Dumb Light Controller

## Slide 10: Timed Automata
ADD a clock x
Synchronizing action
Clock Guard
Conjunctions of x~n
x: real-valued clock
Reset
[Alur & Dill’89]

## Slide 11: A Timed Automata (Semantics)
States:
( location , x=v) where v2R
Transitions:
( Off , x=0 )
delay 4.32  ( Off , x=4.32 )
press?  ( Light , x=0 )
delay 2.51  ( Light , x=2.51 )
press?  ( Bright , x=2.51 )

## Slide 12: Intelligent Light Controller
Invariant (Henzinger)

## Slide 13: Intelligent Light Controller
Transitions:
( Off , x=0 )
delay 4.32  ( Off , x=4.32 )
press?  ( Light , x=0 )
delay 4.51  ( Light , x=4.51 )
press?  ( Light , x=0 )
delay 100  ( Light , x=100)
  ( Off , x=0)
Note:
( Light , x=0 ) delay 103 
X
Invariants ensures progress

## Slide 14: Train Crossing
Time
River
Bridge
tracks
Safe
Approaching
Crossing
Safe
0
3 – 5
20

## Slide 15: Train Crossing
Time
River
Bridge
tracks
Safe
Approaching
Crossing
Safe
Safe
Approaching
Crossing
Safe
10
0
3 – 5
20
Stop the train while it still stoppable!

## Slide 16: Train Crossing
Time
River
Bridge
tracks
Safe
Approaching
Crossing
Safe
Safe
Approaching
Crossing
Safe
10
0
3 – 5
20
Stopped
Crossing
Safe
Restarted
Stopped
Crossing
Safe
7 – 15
Crossing
Restarted

## Slide 17: Train Crossing
Safe
Approaching
Crossing
Safe
Stopped
Restarted
Add timing+ synchronization

## Slide 18: Timed Automata [Train]
= Finite State Control
+ Real Valued Clocks
invariants
Guards
Synchronizations
Resets
SEMANTICS
( Appr , x=0 ) -5.2->
( Appr , x=5.2 ) –stop? ->
( Stop , x=5.2 )

## Slide 19: DEMO

## Slide 20: Logical Specifications
Validation Properties
  Possibly: E<> P
Safety Properties
  Invariant: A[] P
  Pos. Inv.: E[] P
Liveness Properties
  Eventually: A<> P
  Leadsto: P  Q
Bounded Liveness
  Leads to within: P · t Q
The expressions P and Q must be type safe, side effect free, and evaluate to a boolean.
Only references to integer variables, constants, clocks,
and locations are allowed (and arrays of these).

## Slide 21: THE ”secret” of UPPAAL

## Slide 22: Zones – From Finite to Efficiency
A zone Z: 1· x · 2 Æ
0· y · 2 Æ
x - y ¸ 0

## Slide 23: Zones - Operations
x
y
x
y
x
y
x
y
x
y
x
y
(n, 2·x·4 Æ
1·y·3 Æ y-x·0 )
(n, 2·x Æ
1·y Æ -3· y-x·0 )
(n, 2·x Æ
1·y·3 Æ y-x·0 )
Delay
Delay (stopwatch)
Reset
(n, x=0 Æ 1·y·3 )
Extrapolation
2
Convex Hull
(n, 2·x·4Æ 1·y )

## Slide 24: Datastructures for Zones
Difference Bounded Matrices (DBMs)
Minimal Constraint Form [RTSS97]
Clock Difference Diagrams [CAV99]
x1
x2
x3
x0
-4
4
2
2
5
3
3
-2
-2
1

## Slide 25: Stochastic Timed Automata

## Slide 26: Stochastic Semantics of TA
Uniform Distribution
Exponential Distribution
Input enabled
Composition =
Repeated races between components for outputting
1
2
3
4
5
0.5
1

## Slide 27: Stochastic Semantics of Timed Automata
Delay Density Function
¹s: R! R
Output Probability Function
°s: §o! [0,1]
¹s uniform on [ dmin, dmax ]
°s uniform over enabled outputs
g1
g2
s

## Slide 28: Composition of STA
Composition = Race between components
for outputting
Pr[time<=2](<> T.T3) ?
Pr[time<=T](<> T.T3) ?

## Slide 29: Stochastic Semantics of TA
Assumptions:
Component TAs are:
  Input enabled
  Deterministic
  Disjoint set of output actions
¼ ( s , a1 a2 …. an ) : the set of maximal runs from s with a prefix
t1 a1 t2 a2 … tn ak
for some t1,…,tn 2 R.
Delay Density Function
¹s: R! R
Output Probability Function
°s: §o! [0,1]

## Slide 30: Beyond Uniform / Exponential Dist.
Includes all Phase-Type
Distributions.
Can encode any distribution with
arbitrary precision.

## Slide 31: Statistical Model Checking
M
Á
µ, ²
Generate random run
Validate
Core Statistical
Algorithm
Inconclusive
PrM(Á) 2 [a-²,a+²]
with confidence µ
p,®
PrM(Á) ¸ p
at significance level ®
}<T p
[FORMATS11,
LPAR12, RV12]
Confidence
Interval
Hypothesis
testing

## Slide 32: Queries in UPPAAL Syntax
Evaluation Pr[<=100](<> expr)
Hypothesis testing Pr[<=100](<> expr)>=0.1 c<=100 #<=50 [] expr <=0.5
Comparison Pr[<=20](<> e1)>=Pr[<=10](<> e2)
Expected value E[<=10;1000](min: expr) Explicit number of runs. Min or max.
Simulations simulate 10 [<=100]{expr1,expr2}

## Slide 33: DEMO

## Slide 34: Stochastic Hybrid Systems
A Bouncing Ball
Player 1
Player 2

## Slide 35: Stochastic Hybrid Systems
A Bouncing Ball
Ball
Player 1
Player 2
simulate 1 [<=20]{Ball1.p, Ball2.p}
Pr[<=20](<>(time>=12 && Ball1.p>4))
Pr[<=20](<> (time>=12 && Ball1.p>4)) >= Pr[<=20](<> (time>=12 && Ball2.p>4))

## Slide 36: Stochastic Hybrid Systems
on/off
on/off
Room 1
Room 2
Heater
simulate 1 [<=100]{Temp(0).T, Temp(1).T}
simulate 10 [<=100]{Temp(0).T, Temp(1).T}
Pr[<=100](<> Temp(0).T >= 10)
Pr[<=100](<> Temp(1).T<=5 and time>30) >= 0.2

## Slide 37: Stochastic Hybrid Systems
A Bouncing Ball
Ball
Player 1
Player 2
simulate 1 [<=20]{Ball1.p, Ball2.p}
Pr[<=20](<>(time>=12 && Ball.p>4))
UPPAAL SMC
Uniform distributions (bounded delay)
Exponential distributions (unbounded delay)
Syntax for discrete probabilistic choice
Distribution on next state by use of random
GUI for plot composing and exporting
Hybrid flow by use of ODEs
+ usual stuff (structured variables, user-defined types
user-defined functions, ….)
MITL
Networks
Repeated races between components for outputting

## Slide 38: Schedulability & Performance Analysis
??

## Slide 39: Task Scheduling
T2 is running
{ T4 , T1 , T3 } ready ordered according to some
given priority: (e.g. Fixed Priority, Earliest Deadline,..)
T1
T2
Tn
Scheduler
2
1
4
3
ready
done
stop
run
P(i), UNI[E(i), L(i)], .. : period or earliest/latest arrival or .. for Ti
C(i), UNI[BC(i),WC(i)] : execution time for Ti
D(i): deadline for Ti
utilization of CPU

## Slide 40: Modeling Task
T1
T2
Tn
Scheduler
2
1
4
3
ready
done
stop
run

## Slide 41: Modeling Scheduler
T1
T2
Tn
Scheduler
2
1
4
3
ready
done
stop
run

## Slide 42: Modeling Queue
T1
T2
Tn
Scheduler
2
1
4
3
ready
done
stop
run
……

## Slide 43: Schedulability Analysis
const int E[N] = { 200, 200, 100, 100 };
const int L[N] = { 400, 200, 100, 100 }; // Ready interval
const int D[N] = { 400, 200, 100, 100 }; // Deadlines
const int WC[N] = { 60, 40, 20, 10 }; // Worst Computation Times
const int BC[N] = { 20, 20, 10, 5 }; // Best Computation Times
const int P[N] = { 1, 2, 3, 4 }; // Priorities
simulate 1 [<=400]
{ Task0.Ready + 2*Task0.Running +3*Task0.Blocked,
Task1.Ready + 2*Task1.Running +3*Task1.Blocked + 4,
Task2.Ready + 2*Task2.Running + 3*Task2.Blocked + 8,
Task3.Ready + 2*Task3.Running + 3*Task3.Blocked +12 }
A[] not (Task0.Error or Task1.Error or Task2.Error or Task3.Error)


## Slide 44: Schedulability Analysis
const int E[N] = { 200, 200, 100, 100 };
const int L[N] = { 400, 200, 100, 100 }; // Ready interval
const int D[N] = { 400, 200, 100, 100 }; // Deadlines
const int WC[N] = { 60, 40, 20, 60 }; // Worst Computation Times
const int BC[N] = { 20, 20, 10, 5 }; // Best Computation Times
const int P[N] = { 1, 2, 3, 4 }; // Priorities
A[] (not Taski.Error) i : 0,1,2,3

Pr[<=4000] ( <> Task0.Error or Task1.Error or Task2.Error or Task3.Error)
simulate 10000 [<=400]
{ Task0.Ready + 2*Task0.Running +3*Task0.Blocked,
Task1.Ready + 2*Task1.Running +3*Task1.Blocked + 4,
Task2.Ready + 2*Task2.Running + 3*Task2.Blocked + 8,
Task3.Ready + 2*Task3.Running + 3*Task3.Blocked +12 }
: 1 : (Task0.Error or Task1.Error or Task2.Error or Task3.Error)




## Slide 45: Performance Analysis
sup : Task2.r, Task3.r

## Slide 46: Performance Analysis
E[<=800; 5000] (max: Task0.r)
E[<=800; 5000] (max: Task0.r)
E[<=800; 5000] (max: Task0.r)
E[<=800; 5000] (max: Task0.r)
D=400
D=200
D=100
D=100

## Slide 47: Herschel-Planck Scientific Mission at ESA
Attitude and Orbit Control Software
TERMA A/S Steen Ulrik Palm, Jan Storbank Pedersen, Poul Hougaard

## Slide 48: Herschel & Planck Satelites
Application software (ASW)
  built and tested by Terma:
  does attitude and orbit control, tele-commanding, fault detection isolation and recovery.
Basic software (BSW)
  low level communication and scheduling periodic events.
Real-time operating system (RTEMS)
  Priority Ceiling for ASW,
  Priority Inheritance for BSW
Hardware
  single processor, a few communication buses, sensors and actuators.
Requirements:
  Software tasks should be schedulable.
  CPU utilization should not exceed 50% load

## Slide 49: Modeling in UPPAAL
UPPAAL 4.1 Framework
ISoLA 2010

## Slide 50: Gantt Chart 1. cycle

## Slide 51: Blocking & WCRT
Marius Micusionis

## Slide 52: Effort and Utilization
Marius Micusionis

## Slide 53: TERMA Case Conclusion

## Slide 54: TERMA Case Follow-Up
[ f*WCET, WCET]
1 Day
6 Days
f=100%
f=95%
f=90%
f=86%
ISOLA 2012

## Slide 55: TERMA Case - Statistical MC

## Slide 56: TERMA Case – Conclusion

## Slide 57: Timed Games
TIGA
Notes: FSEN’09
This talk will introduce various recent extensions of the by know well-established formalism of timed automata. The talk apply these extension to verification, optimal scheduling, performance analysis and controller synthesis of real-time and embedded systems. The timed automata extensions considered -- priced timed automata, game timed automata as well as probabilistic timed automata -- are all supported by various branches of the real-time verificaiton tool UPPAAL (www.uppaal.com) which will be demonstrated during the talk. Also, the development of algorithms and datastructures applied by UPPAAL for the efficient analysis of these models is provided.
Validation, Performance Analysis and Synthesis of Embedded Systems Kim G Larsen Within the upcoming European Joint Technology Initiative ARTEMIS as well as several national initiatives such as CISS (www.ciss.dk) and DaNES (http://www.danes.aau.dk/), model-driven development is a key to dealing with the increasing complexity of embedded systems, while reducing the time and cost to market. The use of models should permit early assessment of the functional correctness of a given design as well as requirements for resources (e.g. energy, memory, and bandwidth) and real-time and performance guarantees. Thus, there is a need for quantitative models allowing for timed, stochastic and hybrid phenomenas to be modeled an analysed. UPPAAL and the branches CORA and TIGA provide an integrated tool environment for modelling, validation, verification and synthesis of real-time systems modelled as networks timed automata, extended with data types and user-defined functions. The talk will provide details on the expressive power of timed automata in relationship to embedded systems as well as details on the power and working of the UPPAAL verification engine. In this talk we demonstrate how UPPAAL has been applied to the validation, performance analysis and synthesis of embedded control problems. The applications include so-called task graph scheduling and MPSoC systems consisting of application software running under different RTOS on processors interconnected through an on-chip network. Also we show how CORA and TIGA has been used to synthesize optimal (e.g. wrt. energy or memory) scheduling strategies given applications, including Dynamic Voltage Scaling and a climate controller.

## Slide 58: Timed Automata & Model Checking
State (L1, x=0.81)
Transitions
(L1 , x=0.81)
- 2.1 ->
(L1 , x=2.91)
->
(goal , x=2.91)
Ehi goal ?
Ahi goal ?
A[ ] : L4 ?

## Slide 59: Timed Game Automata & Synthesis
Problems to be considered:
Does there exist a winning strategy?
- If yes, compute one (as simple as possible)
controllable
uncontrollable

## Slide 60: Computing Winning States

## Slide 61: Decidability of Timed Games

## Slide 62: Model Checking (ex Train Gate)
: Never two trains at
the crossing at the
same time
Environment
Controller

## Slide 63: Synthesis (ex Train Gate)
: Never two trains at
the crossing at the
same time
Environment
Controller
?

## Slide 64: Timed Games
: Never two trains at
the crossing at the
same time
Controllable
Uncontrollable
Find strategy for controllable
actions st behaviour satisfies 
Controller
Environment

## Slide 65: A Buggy Brick Sorting Program
Conveyer Belt
eject
BUGGY

## Slide 66: Brick Sorting
Piston
Generic Plate
Controller

## Slide 67: Brick Sorting
Piston
Generic Plate
Controller
Strategy for EJECT

## Slide 68: Production Cell Overview
Realistic case- study described in several formalisms (1994 and later).
Objective: stamp metal plates in press.
feed belt, two-armed robot, press, and deposit belt.

## Slide 69: Production Cell in UPPAAL Tiga

## Slide 70: Experimental Results
[CDF+05]
[BCD+07]

## Slide 71: Plastic Injection Molding Machine
Robust and optimal control
Tool Chain
  Synthesis: UPPAAL TIGA
  Verification: PHAVer
  Performance: SIMULINK
40% improvement of existing solutions..
Quasiomodo
[CJL+09]

## Slide 72: Oil Pump Control Problem
R1: stay within safe interval [4.9,25.1]
R2: minimize average/overall oil volume
Quasiomodo

## Slide 73: The Machine (consumption)
Infinite cyclic demand to be satisfied by our control strategy.
P: latency 2 s between state change of pump
F: noise 0.1 l/s
Quasiomodo

## Slide 74: Hybrid Game Model
Undecidability

Discretization

## Slide 75: Abstract Game Model
UPPAAL Tiga offers games of perfect information
Abstract game model such that states only contain information about:
  Volume of oil at the beginning of cycle
  The ideal volume as predicted by the consumption cycle
  Current time within the cycle
  State of the Pump (on/off)
  Discrete model
D
V, V_rate
V_acc
time
Quasiomodo

## Slide 76: Machine (uncontrollable)
Checks whether V under noise gets outside [Vmin+0.1,Vmax-0.1]
Quasiomodo

## Slide 77: Pump (controllable)
Every 1 (one)
seconds
Quasiomodo

## Slide 78: Global Approach
Find some interval I1=[V1,V2] µ [4.9,25.1] s.t
I1 is m-stable i.e. from any V0 in I1 there is strategy st whatever fluctuation volume is always within [5,25] and at the end within I2=[V1+m,V1-m]
I1 is optimal among all m-stable intervals.
0
25
5
10
15
20
I1
I2
0 s
20 s
Queries ( min. K )
control: A} ( time=20 Æ not BAD Æ V2 I2 Æ V_acc· K )

## Slide 79: Tool Chain
Strategy Synthesis TIGA
Verification PHAVER
Performance Evaluation
SIMULINK
Guaranteed
Correctness
Robustness
with
40% Improvement
Quasiomodo

## Slide 80: Tool Chain
Strategy Synthesis TIGA
Verification PHAVER
Performance Evaluation
SIMULINK
Guaranteed
Correctness
Robustness
with
40% Improvement
Quasiomodo

## Slide 81: Stochastic Priced Timed Games

## Slide 82: Going to Sydney – in 1 hour
0.9
0.9
0.1
0.1
U[42,45]
U[0,35]
U[0,20]
U[0,140]
Can I get to Sidney?
(1-player)
Will I always come to Sidney?
(1-player)
What is the optimal WC strategy?
(2-player)
Is there a strategy guaranteeing
WC <= 60?
(2-player)
What is the optimal strategy?
(1½-player)
What is the optimal strategy
Guarenteeing WC <= 60?
(1½-player)

## Slide 83
G
Timed Game
σ
Strategy
P
Stochastic Priced
Timed Game
P|σ
φ
synthesis
abstraction
σ°
optimized
Strategy
G|σ
Timed Automata
P|σ°
Stochastic Priced Timed Automata
minE(cost)
maxE(gain)
Uppaal TIGA
  strategy NS = control: A<> goal
  strategy NS = control: A[] safe
Statistical Learning
strategy DS = minE (cost) [<=10]: <> done under NS
strategy DS = maxE (gain) [<=10]: <> done under NS
Uppaal
  E<> error under NS
  A[] safe under NS
Uppaal SMC
simulate 5 [<=10]{e1, e2} under SS Pr[<=10](<> error) under SS E[<=10;100](max: cost) under SS

## Slide 84: – DEMO
control: A<> Kim.Sidney && time<=60

## Slide 85: Safe & Adaptive Cruice Control
Q1: Find a safety strategy for Ego such no crash will ever occur no matter what Front is doing.
Q2: Find the most permissive strategy ensuring safety
Q3: Find the optimal sub-strategy that will allow Ego to go as far as possible (without overtaking).
EGO
FRONT

## Slide 86: Discretization
Discrete
Continuous

## Slide 87: Ego

## Slide 88: Front

## Slide 89: No Strategy

## Slide 90: Safety Strategy

## Slide 91: Safety Strategy

## Slide 92: Optimal and Safe Strategy

## Slide 93: Other Case Studies
FIREWIRE
BLUETOOTH
10 node LMAC
Battery
Scheduling
Energy Aware
Buildings
Genetic Oscilator
(HBS)
Passenger
Seating in
Aircraft
Schedulability
Analysis for
Mix Cr Sys
Smart Grid
Demand /
Response

## Slide 94: LASSO Learning, Analysis, SynthesiS and Optimization of Cyber-Physical Systems
Contact: kgl@cs.aau.dk

## Slide 95: www.uppaal.org

## Slide 96: Applications

## Slide 97: Case Studies: Controllers
Memory Arbiter Synthesis and Verification for a Radar Memory Interface Card, 2005
Analyzing a χ model of a turntable system using Spin, CADP and Uppaal, 2006
Designing, Modelling and Verifying a Container Terminal System Using UPPAAL, 2008
Model-based system analysis using Chi and Uppaal: An industrial case study, 2008
Climate Controller for Pig Stables, 2008 (synth)
Optimal and Robust Controller for Hydralic Pump, 2009 (synth)

## Slide 98: References
Frits Vaandrager: A first introduction to UPPAAL
Alexandre David, Kim G Larsen: More features in UPPAAL
Alexandre David, Kim G Larsen, Axel Legay, Marius Mikucionis, Danny Bøgsted Poulsen: UPPAAL SMC Tutorial. To appear in Software Tools for Technology Transfer.
Alexandre David, Kim G. Larsen, Axel Legay, Marius Mikucionis, Zheng Wang: Time for Statistical Model Checking of Real-Time Systems. CAV 2011.
Gerd Behrmann, Agnes Cougnard, Alexandre David, Emmanuel Fleury, Kim G. Larsen, and Didier Lime: UPPAAL-Tiga: Time for Playing Games! CAV 2007.
Alexandre David, Peter Gjøl Jensen, Kim Guldstrand Larsen, Marius Mikucionis, Jakob Haahr Taankvist: Uppaal Stratego. TACAS 2015
For more see
  http://people.cs.aau.dk/~kgl/SSFT2015/

## Slide 99: Case Studies: Protocols
Analysis of a protocol for dynamic configuration of IPv4 link local addresses using Uppaal, 2006
Formalizing SHIM6, a Proposed Internet Standard in UPPAAL, 2007
Verifying the distributed real-time network protocol RTnet using Uppaal, 2007
Analysis of the Zeroconf protocol using UPPAAL, 2009
Analysis of a Clock Synchronization Protocol for Wireless Sensor Networks, 2009
Model Checking the FlexRay Physical Layer Protocol, 2010

## Slide 100: Using UPPAAL as Back-end
Timed automata translator from Uppaal to PVS
Component-Based Design and Analysis of Embedded Systems with UPPAAL PORT, 2008
METAMOC: Modular WCET Analysis Using UPPAAL, 2010.
TetaSARTS: a tool for modular timing analysis of safety critical Java systems, 2013

## Slide 101: www.uppaal.{org,com}
THANKS !